## Slide 1: AT Command of HC-06
Installation of Arduino Pro Micro

## Slide 2: Step 1:
Wire up the connections as shown in the diagram.

## Slide 3: Step 2:
Open up
1
Open up the AT_Command_HC-06 ino file
Read
2
Read the instructions carefully before running the program
Refer
3
Refer to the next two slides for more information regarding the AT Command of HC-06.

## Slide 4: AT Commands Instructions
AT Commands Available:
AT : check the connection
AT+NAME: Change name. No space between name and command.
AT+BAUDX: change baud rate, X is baud rate code, no space between command and code.
AT+PINXXXX: change pin, XXXX is the pin, again, no space.
AT+VERSION

## Slide 5: Baudrate Avaliable:
To change baud rate, type AT+BAUDX, where X=1 to 9.
1 set to 1200bps
2 set to 2400bps
3 set to 4800bps
4 set to 9600bps (Default)
5 set to 19200bps
6 set to 38400bps
7 set to 57600bps
8 set to 115200bps
9 set to 230400bps