## Slide 1: DIP Uavionics Phase 1
Installation of Arduino Pro Micro
AT Command of HC-06

## Slide 2: In this 4 weeks, you will be able to…
Design and build your very own Unmanned Ground Vehicle (UGV).
Establish a wireless communication between a microcontroller and your Android phone.
Write a program to maneuver your UGV and collect data for you!

## Slide 3: Components Provided
Arduino Pro Micro w/ cable x1
Motor Driver x1
Bluetooth Module x1
RFID Reader x1
Jumper Cables
Corrugated Plastic (A3 size) x0.5
Wheels x2
DC Motors w/ Brackets x2
Ball Caster Plastic x1
AAA Batteries (100%) x6
3AAA Battery Carriage x2
Mini Breadboard x1
Components Unprovided
Android Phone (minimum 5 inch) x1
Laptop x1
Google mail account x1
Miscellaneous equipment
eg. Scissors, pen, pencil, markers, etc

## Slide 4
Arduino Pro Micro
5V, 16MHz
RFID Reader RDM6300
5V, 125kHz
Motor Driver TB6612FNG
5V VCC, 15V VM, 1.2-3.2 A
GP Rechargeable Battery
AAA, 800mAh, 1.2V
Micro Metal Gear Motor
50:1
Bluetooth Module HC-06
5V, 2.4GHz, 9600bps
Note that all the descriptions above are summarized and simplified.
For more detailed and accurate information, please refer to individual datasheets or official websites.

## Slide 5: Building Procedures
Step 1:
Solder the male-to-male wires to the DC motors
Wire
DC Motor
Soldering Tutorial (Recommended):
https://youtu.be/f95i88OSWB4

## Slide 6: Building Procedures
Step 2:
Creating the body of the bot and the wheels
Cut the corrugated sheet into 2-4 small pieces
Feel free to change the shapes and sizes
After cutting, stack and attach the layers together

## Slide 7: Building Procedures
Step 2:
*Hints*
Holes like this can be drilled across the boards for neater connections
Position the castor ball at the front of the car
Secure the brackets onto each side of the UGV

## Slide 8: Building Procedures
Step 2:
Insert the motors through the bracket
Attached the wheels to the motors

## Slide 9: Building Procedures
Step 3:
Assemble the electronics
Solder the necessary components according to the schematic diagram shown on the next slide
Usage of mini breadboard is optional
Sample
Sample
These samples are for illustration purposes only, please do not use them as your wiring reference

## Slide 10
Wiring Diagram
Do note that the schematic above is for reference only. You may reconstruct the circuit based on your UGV to achieve better performance.

## Slide 11: Building Procedures
Step 3:
Be creative with the placement of your components!
Make them neat, tidy and efficient!

## Slide 12: Building Procedures
Step 4:
Download Android Interface
  *Note that this app only work on Android products and the link can only be access after you login using a Gmail account*
  Device with at least a 5” screen is recommended
  Link to MIT app inventor:
    http://bit.ly/2uTEFzI

## Slide 13: Building Procedures
Step 4:
Download Android Interface
Once you login, click on Gallery and search for ‘Uavionics DIP Phase 1 2017’
Select the icon shown on the left then click on ‘OPEN THE APP’
Name the APP as your group name and click ‘OK’

## Slide 14: Building Procedures
Step 4:
Download Android Interface
You should see an interface like this ->
Click on Build>App ( provide QR code for .apk)

## Slide 15: Building Procedures
Step 4:
Download Android Interface
Scan the QR code using you Android phone
Once done, install the app onto your Android phone
*Note that you may need to adjust your phone security setting in order to install the app*
Checkout the link below if you have trouble with the installation:
  http://bit.ly/2tGglS3

## Slide 16: Building Procedures
Step 5:
Testing of Connectivity
After the installation, run the app and your should see a similar interface as shown on the right.
Power up your Arduino via USB cable and touch on the ‘Connect’ button
Search for your device name and enter the PIN number, your device should be connected after a few seconds

## Slide 17: Building Procedures
Step 6:
Download Arduino Code
Click on ‘DOWNLOAD ALL’ on the top right corner of the window and unzip the zip file.
Do not change the file name, make sure the 2 INO files are kept in a single folder
Click on either INO file and open it using Arduino IDE
Your window should consists of 2 tabs ->>
As for now, you can ignore the first tab and click on the second tab
  Link to Arduino code:
  http://bit.ly/2vERs6B

## Slide 18: Building Procedures
Here are the functions available for you to call.
Each function will perform a specify task. Eg. Calling Forward() in the main loop will instruct your UGV to move forward

## Slide 19: Building Procedures
Here are the commands available for your UGV to know what you have pressed on your interface.
Each command represents a specify button on your interface. Eg. Writing a ‘if loop’ with a condition of (Forward_Pressed()) simply means ‘if the forward button is pressed on your interface’

## Slide 20: Building Procedures
Here is the part that you have to complete.
Basically, you are task to write out an algorithms on how your UGV should react to your commands.
Codes written in this loop will only be run once
Codes written in this loop will be run continuously
Please enter your group name here
*Hints*
No clues on how to begin with? Get some help here!
https://www.arduino.cc/en/Reference/HomePage